## Slide 1: Thin Lift Asphalt Overlays
Christie Bishop Barbee
Joint Asphalt Training
March 24, 2010

## Slide 2: Maintenance Using HMA
Contract Resurfacing
$300 million
2nd Largest State Maintained System
79,000 miles
Total Resurfacing Needs
$450 MILLION

## Slide 3: Preventive Maintenance
System Preservation
$100 million
Approved Uses of Funds
Micro-surfacing
Chip Seals
HIP Recycling
Novachip
Asphalt Overlays

## Slide 4: Looking for Solutions
Preservation funds are being used to address resurfacing needs
  Micro-surfacing
  HIP Recycling
  Thin Asphalt Overlays
  Novachip

## Slide 5: Micro-surfacing
Polymer modified slurry seal
Placed at rate of 24 lbs. per square yard
Homeowners and motorists don’t like it
Life Expectancy of 5-7 years

## Slide 6: Looking for Solutions
Preservation funds are being used to address resurfacing needs
  Micro-surfacing
  HIP Recycling
  Thin Asphalt Overlays
  Novachip

## Slide 7: HIP Recycling
Has a place in our arsenal
Pavements with limited deterioration
Pavements with uniform mix
Does not add structure
Problems with certain mixes
Environmental concerns

## Slide 8: HMA Alternative
Must be competitive in cost
Must perform as well or better
Must use readily available materials
Other States
Ohio – Smoothseal
Michigan – Preventive Maintenance HMA

## Slide 9: S 4.75A Mix
“Sand Asphalt”
Predominately a resurfacing mix
Uses aggregate screenings
Public loves it – Smooth ride, looks good
10-12 yr life expectancy
NC has some 18+ yr. 4.75 pavements

## Slide 10: Advantages of S 4.75A Mix
Smoothness
Longer Life
Increased Strength
Better for the Environment
Cost Effective
Ease of Use

## Slide 12
Description | $/sy | Cost/Mile (24’ wide) | Life Extension (Years) | Cost/Mile/Year | Application Rate
Micro-surfacing |  |  |  |  | 
June 2008 | $2.50 | $35,200 | 5 | $7,040 | 24#/sy
June 2008 | $2.76 | $38,861 | 5 | $7,772 | 24#/sy
Thin-Lift Asphalt | AC adjusted for June 2008 |  |  |  | 
April 2008 | $2.72 | $38,298 | 10 | $3,829 | 70#/sy
December 2007 | $2.66 | $37,453 | 10 | $3,745 | 70#/sy
July 2008 | $2.79 | $39,283 | 10 | $3,928 | 70#/sy
July 2008 | $2.75 | $38,720 | 10 | $3,872 | 70#/sy
Preventive Maintenance Treatment Cost Comparison

## Slide 13: Looking for Solutions
Preservation funds are being used to address resurfacing needs
  Micro-surfacing
  HIP Recycling
  Thin Asphalt Overlays
  Novachip

## Slide 14
Novachip
Concrete
has performed well
HMA
no good reason
Expensive
Patent on process
Availability
materials
paver

## Slide 15: HMA Alternative
Must be competitive in cost
Must perform as well or better
Must use readily available materials
Solution
OGFC
Quieter
Safer
Cooler

## Slide 16: Why Asphalt?
Funding Crisis Places Emphasis on Preservation and Maintenance
Cost Effective
Black is Green
Provides Good Jobs for NC Workers

## Slide 17
Thank you!